## Slide 1
1
WAP - Wireless Application Protocol
Goals
deliver Internet content and enhanced services to mobile devices and users (mobile phones, PDAs)
independence from wireless network standards
open for everyone to participate, protocol specifications will be proposed to standardization bodies
applications should scale well beyond current transport media and device types and should also be applicable to future developments
Platforms
e.g., GSM (900, 1800, 1900), CDMA IS-95, TDMA IS-136, 3rd
generation systems (IMT-2000, UMTS, W-CDMA, cdma2000 1x EV-DO, …)
Forum
was: WAP Forum, co-founded by Ericsson, Motorola, Nokia, Unwired Planet, further information www.wapforum.org
now: Open Mobile Alliance www.openmobilealliance.org (Open Mobile Architecture + WAP Forum + SyncML + …)
WAP - scope of standardization
Browser
“micro browser”, similar to existing, well-known browsers in the Internet
Script language
similar to Java script, adapted to the mobile environment
WTA/WTAI
Wireless Telephony Application (Interface): access to all telephone functions
Content formats
e.g., business cards (vCard), calendar events (vCalender)
Protocol layers
transport layer, security layer, session layer etc.
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.22

## Slide 4
WAP 1.x - reference model and protocols
Bearers (GSM, CDPD, ...)
Security Layer (WTLS)
Session Layer (WSP)
Transport Layer (WDP)
TCP/IP, UDP/IP,
media
SSL/TLS
HTML, Java Application Layer (WAE)
HTTP
Internet WAP
WAE comprises WML (Wireless Markup Language), WML Script, WTAI etc.
Transaction Layer (WTP)
additional services and applications
WCMP
A-SAP
S-SAP
TR-SAP
SEC-SAP
T-SAP
WAP - network elements
wireless network
fixed network
WAP
proxy
WTA
server
filter/
WAP
proxy
web server
filter
Internet
PSTN
Binary WML: binary file format for clients
Binary WML
Binary WML
Binary WML
HTML
HTML
HTML
WML
WML
HTML
10.24

## Slide 5
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.25
WDP - Wireless Datagram Protocol
Protocol of the transport layer within the WAP architecture
uses directly transports mechanisms of different network technologies
offers a common interface for higher layer protocols
allows for transparent communication using different transport technologies (GSM [SMS, CSD, USSD, GPRS, ...], IS-136, TETRA, DECT, PHS, IS-95,
...)
Goals of WDP
create a worldwide interoperable transport system with the help of WDP adapted to the different underlying technologies
transmission services such as SMS, GPRS in GSM might change, new services can replace the old ones
Additionally, WCMP (wireless Control Message Protocol) is used for control/error report (similar to ICMP in the TCP/IP protocol suite)
WDP - Service Primitives
T-SAP
T-SAP
T-DUnitdata.req
(DA, DP, SA, SP, UD)
T-DUnitdata.ind (SA, SP, UD)
T-DUnitdata.req
(DA, DP, SA, SP, UD)
T-DError.ind (EC)
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.26

## Slide 6
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.27
Usage of WDP
GSM-SMS
GSM-CSD
WTLS
WTLS
WDP &
Adaptation
WDP &
Adaptation
SMS
SMS
Wireless Data Gateway
WTLS
WTLS
WDP &
Adaptation
WDP &
Adaptation
Tunnel
Tunnel
Subnetwork
Subnetwork
SMS
SMS
Tunnel
Tunnel
Subnetwork
Subnetwork
WAP
Proxy
WTLS
WTLS
UDP
UDP
WTLS
WTLS
UDP
UDP
IP
IP
PPP
PPP
CSD-RF
CSD-RF
IP
IP
Subnetwork
Subnetwork
IP
IP
PPP
PPP
CSD-RF
CSD-RF
PSTN
Circuit
PSTN
Circuit
Subnetwork
Subnetwork
Interworking Function
Internet Service Provider Remote Access Service
PSTN
Circuit
PSTN
Circuit
WTLS - Wireless Transport Layer Security
Goals
data integrity
  prevention of changes in data
privacy
  prevention of tapping
authentication
  creation of authenticated relations between a mobile device and a server
protection against denial-of-service attacks
  protection against repetition of data and unverified data
WTLS
is based on the TLS (Transport Layer Security) protocol (former SSL, Secure Sockets Layer)
optimized for low-bandwidth communication channels
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.28

## Slide 7
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.29
Secure session, full handshake
SEC-Create.req
(SA, SP, DA, DP, KES, CS, CM)
originator SEC-SAP
peer SEC-SAP
SEC-Create.ind
(SA, SP, DA, DP, KES, CS, CM)
SEC-Create.res
(SNM, KR, SID, KES‘, CS‘, CM‘)
SEC-Exchange.req
SEC-Create.cnf
(SNM, KR, SID, KES‘, CS‘, CM‘)
SEC-Exchange.ind
SEC-Exchange.res (CC)
SEC-Commit.req
SEC-Exchange.cnf (CC)
SEC-Commit.ind
SEC-Commit.cnf
SEC-Unitdata - transferring datagrams
SEC-Unitdata.req (SA, SP, DA, DP, UD)
SEC-Unitdata.ind (SA, SP, DA, DP, UD)
sender SEC-SAP
receiver SEC-SAP
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.30

## Slide 8
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.31
WTP - Wireless Transaction Protocol
Goals
different transaction services, offloads applications
  application can select reliability, efficiency
support of different communication scenarios
  class 0: unreliable message transfer
  class 1: reliable message transfer without result message
  class 2: reliable message transfer with exactly one reliable result message
supports peer-to-peer, client/server and multicast applications
low memory requirements, suited to simple devices (< 10kbyte )
efficient for wireless transmission
  segmentation/reassembly
  selective retransmission
  header compression
  optimized connection setup (setup with data transfer)
Details of WTP I
Support of different communication scenarios
Class 0: unreliable message transfer
  Example: push service
Class 1: reliable request
  An invoke message is not followed by a result message
  Example: reliable push service
Class 2: reliable request/response
  An invoke message is followed by exactly one result message
  With and without ACK
  Example: typical web browsing
No explicit connection setup or release is available Services for higher layers are called events
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.32

## Slide 9
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.33
Details of WTP II
Used Mechanisms
Reliability
  Unique transaction identifiers (TID)
  Acknowledgements
  Selective retransmission
  Duplicate removal
Optional: concatenation & separation of messages
Optional: segmentation & reassembly of messages
Asynchronous transactions
Transaction abort, error handling
Optimized connection setup (includes data transmission)
WTP Class 0 transaction
TR-Invoke.req
(SA, SP, DA, DP, A, UD, C=0, H)
Invoke PDU
TR-Invoke.ind
(SA, SP, DA, DP, A, UD, C=0, H‘)
initiator TR-SAP
responder TR-SAP
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.34

## Slide 10
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.35
WTP Class 1 transaction, no user ack & user ack
TR-Invoke.req
(SA, SP, DA, DP, A, UD, C=1, H)
Invoke PDU
TR-Invoke.ind
(SA, SP, DA, DP, A, UD, C=1, H‘)
initiator TR-SAP
responder TR-SAP
Ack PDU
TR-Invoke.req
(SA, SP, DA, DP, A, UD, C=1, H)
Invoke PDU
initiator TR-SAP
responder TR-SAP
Ack PDU
TR-Invoke.ind
(SA, SP, DA, DP, A, UD, C=1, H‘)
TR-Invoke.res (H‘)
TR-Invoke.cnf (H)
TR-Invoke.cnf (H)
WTP Class 2 transaction, no user ack, no hold on
TR-Invoke.req
(SA, SP, DA, DP, A, UD, C=2, H)
Invoke PDU
initiator TR-SAP
responder TR-SAP
Result PDU
TR-Invoke.ind
(SA, SP, DA, DP, A, UD, C=2, H‘)
TR-Result.req (UD*, H‘)
Ack PDU
TR-Invoke.cnf (H)
TR-Result.ind (UD*, H)
TR-Result.res (H)
TR-Result.cnf (H‘)
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.36

## Slide 11
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.37
WTP Class 2 transaction, user ack
TR-Invoke.req
(SA, SP, DA, DP, A, UD, C=2, H)
Invoke PDU
initiator TR-SAP
responder TR-SAP
Result PDU
Ack PDU
Ack PDU
TR-Invoke.ind
(SA, SP, DA, DP, A, UD, C=2, H‘)
TR-Invoke.res (H‘)
TR-Result.req (UD*, H‘)
TR-Invoke.cnf (H)
TR-Result.ind (UD*, H)
TR-Result.res (H)
TR-Result.cnf (H‘)
WTP Class 2 transaction, hold on, no user ack
TR-Invoke.req
(SA, SP, DA, DP, A, UD, C=2, H)
Invoke PDU
TR-Invoke.ind
(SA, SP, DA, DP, A, UD, C=2, H‘)
initiator TR-SAP
responder TR-SAP
Result PDU
TR-Result.req (UD*, H‘)
Ack PDU
Ack PDU
TR-Invoke.cnf (H)
TR-Result.ind (UD*, H)
TR-Result.res (H)
TR-Result.cnf (H‘)
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.38

## Slide 12
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.39
WSP - Wireless Session Protocol
Goals
HTTP 1.1 functionality
  Request/reply, content type negotiation, ...
support of client/server, transactions, push technology
key management, authentication, Internet security services
session management (interruption, resume,...)
Open topics
QoS support)
Group communication
Isochronous media objects
management
WSP protocols
WSP
Connection mode (uses WTP)
Connectionless mode (uses WDP or WTLS)
Session Management (class 0, 2)
Method Invocation (Kl. 2)
Error Report
Push (class 0)
Confirmed Push (class 1)
Session suspend/resume (class 0, 2)
Method Invocation
Push
(in general unreliable)
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.40

## Slide 13
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.41
WSP/B session establishment
S-Connect.req (SA, CA, CH, RC)
Connect PDU
client S-SAP
server S-SAP
ConnReply PDU
S-Connect.ind (SA, CA, CH, RC)
S-Connect.res (SH, NC)
S-Connect.cnf (SH, NC)
WTP Class 2 transaction
WSP/B session suspend/resume
Suspend PDU
S-Suspend.ind (R)
client S-SAP
server S-SAP
Reply PDU
WTP Class 2 transaction
S-Suspend.req
S-Suspend.ind (R)
~
S-Resume.req (SA, CA)
~
S-Resume.ind (SA, CA)
S-Resume.res
Resume PDU
S-Resume.cnf
WTP Class 0 transaction
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.42

## Slide 14
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.43
WSP/B session termination
Disconnect PDU
S-Disconnect.ind (R)
client S-SAP
server S-SAP
WTP Class 0 transaction
S-Disconnect.req (R)
S-Disconnect.ind (R)
WSP/B method invoke
S-MethodInvoke.req (CTID, M, RU)
Method PDU
client S-SAP
server S-SAP
Reply PDU
WTP Class 2 transaction
S-MethodInvoke.ind (STID, M, RU)
S-MethodInvoke.res (STID)
S-MethodResult.req (STID, S, RH, RB)
S-MethodInvoke.cnf (CTID)
S-MethodResult.ind (CTID, S, RH, RB)
S-MethodResult.res (CTID)
S-MethodResult.cnf (STID)
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.44

## Slide 15
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.45
WSP/B over WTP - method invocation
client S-SAP
server S-SAP
S-MethodInvoke.cnf
S-MethodResult.ind
S-MethodResult.res
S-MethodInvoke.req TR-Invoke.req
initiator TR-SAP
TR-Result.ind
TR-Invoke.cnf
TR-Result.res
responder TR-SAP
TR-Invoke.ind S-MethodInvoke.ind
TR-Invoke.res S-MethodInvoke.res
TR-Result.req S-MethodResult.req
TR-Result.cnf S-MethodResult.cnf
Invoke(Method)
Result(Reply)
Ack PDU
Ack PDU
WSP/B over WTP - asynchronous, unordered requests
client S-SAP
server S-SAP
S-MethodInvoke_1.req S-MethodInvoke_2.req
S-MethodInvoke_3.req
S-MethodResult_1.ind S-MethodResult_3.ind S-MethodInvoke_4.req
S-MethodResult_4.ind S-MethodResult_2.ind
S-MethodInvoke_2.ind S-MethodInvoke_1.ind S-MethodResult_1.req S-MethodInvoke_3.ind
S-MethodResult_3.req S-MethodResult_2.req
S-MethodInvoke_4.ind S-MethodResult_4.req
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.46

## Slide 16
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
MC SS02
10.47
WSP/B - confirmend/non-confirmed push
client S-SAP
server S-SAP
S-Push.req (PH, PB)
ConfPush PDU
WTP Class 1 transaction
S-Push.ind (PH, PB)
S-ConfirmedPush.ind (CPID, PH, PB)
S-ConfirmedPush.res (CPID)
WTP Class 0 transaction
Push PDU
client S-SAP
server S-SAP
S-ConfirmedPush.req (SPID, PH, PB)
S-ConfirmedPush.cnf (SPID)
WSP/B over WDP
S-Unit-MethodInvoke.req (SA, CA, TID, M, RU)
client S-SAP
S-Unit-MethodResult.ind (CA, SA, TID, S, RH, RB)
S-Unit-Push.ind
(CA, SA, PID, PH, PB)
server S-SAP
S-Unit-MethodInvoke.ind (SA, CA, TID, M, RU)
S-Unit-MethodResult.req (CA, SA, TID, S, RH, RB)
S-Unit-Push.req
(CA, SA, PID, PH, PB)
Method PDU
Reply PDU
Push PDU
WDP Unitdata service
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.48

## Slide 17
WAE - Wireless Application Environment
Goals
network independent application environment for low-bandwidth, wireless devices
integrated Internet/WWW programming model with high interoperability
Requirements
device and network independent, international support
manufacturers can determine look-and-feel, user interface
considerations of slow links, limited memory, low computing power, small display, simple user interface (compared to desktop computers)
Components
architecture: application model, browser, gateway, server
WML: XML-Syntax, based on card stacks, variables, ...
WMLScript: procedural, loops, conditions, ... (similar to JavaScript)
WTA: telephone services, such as call control, text messages, phone book, ... (accessible from WML/WMLScript)
content formats: vCard, vCalendar, Wireless Bitmap, WML, ...
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/ MC SS02 10.49
Origin Servers
WAE logical model
web server
other content server
Gateway
Client
other WAE
user agents
WML
user agent
WTA
user agent
encoders & decoders
encoded request
request
encoded response with content
response with content
push content
encoded push content
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/
10.50